| SAFE WORK PRACTICE |
| --- |
| TITLE | Portable Ladders |
| GENERAL | Protecting workers from injuries associated with the use of portable ladders |
| APPLICATION | Portable ladders should only be used when there are no permanent or temporary stairways or work platforms available for task. |
| PROTECTIVE MECHANISMS | Safe work procedure Manufacturers specifications PPE ERP (Emergency Response Plan) |
| SELECTION AND USE | As per safe work procedure Manufacturers specifications Provincial OH&S Legislation |
| SUPERVISOR RESPONSIBILITY | Supervisors are responsible to facilitate and/or provide proper instruction to their workers on protection requirements and training Work site inspection Selection of equipment |
| WORKER RESPONSIBILITY | All ladders shall be inspected prior to performing a task. Wooden ladders shall not be painted. Conductive metal ladders or wire or wire reinforced wooden ladders shall not be permitted in energized areas. Ensure surface is level and firm. Ensure ladder is tied off and set at the proper angle. Ladders shall not be climbed higher than the second step from the top. Three points of contact should always be maintained when climbing up or down. Ladders should not be erected on boxes, tables, scaffold platforms, man lift platforms or on vehicles. A ladder shall not be placed against an unsafe support. Follow portable ladder safe work procedure step by step. |
| * The information presented in this publication is intended for general use and may not apply to every circumstance. It is not a definitive guide to government regulations and does not relieve persons using this publication from their responsibilities under applicable legislation. The Northern Safety Association does not guarantee the accuracy of, nor assume liability for, the information presented here. Individual counselling and advice are available from the Association. |